Envisaging SphinX:
 expected DEM distributions
for selected solar activity levels
A. Kępa, M. Siarkowski,
B. Sylwester and J. Sylwester
Space Research Centre PAS, Solar Physics Division, Wroclaw, Poland

---
What is DEM?
The determination of Differential Emission Measure distributions (DEM) is groundwork for the detailed analysis of flaring plasma.
The DEM characterizes the distribution of matter according to the temperature T in the volume V and is defined as:
        electron density of plasma
Volume
DEM
Temperature

---
Withbroe-Sylwester algorithm
We calculate using the Withbroe-Sylwester algorithm. This algorithm represents an iterative maximum likelihood procedure in which the next approximation of the DEM distribution, j+1(T), is calculated from preceding one j(T) using the following formula:
 the correction factor
DEM
 the weight function

---
Withbroe-Sylwester algorithm
Sylwester, Schrijver, Mewe, 1980

---
What was dane?
1. We choose 3 flares observed by RESIK
25 January 2003 max ~ 3:10 UT B5.6
22 February 2003 max ~ 9:30 UT C5.8
3 August 2002 max ~ 19:07 UT X1.0

---
RESIK spectra for selected flares
 3 Aug 2002
22 Feb 2003
25 Jan 2003

---
What was dane?
2. Based on RESIK fluxes we calculated DEM distributions
 We selected 19 spectral bands

---
Emission functions
 1 Ar XVII 3p high
 2 Ar XVI 3p sat. high
 3 K XVIII (w) high
 4 K XVIII (z) high
 5 S XVI 5p high
 6 Ar XVIII 2p high
 7 S XVI 4p high
 8 Ar XVII 2p 22
 9 S XV 4p high
10 S XV 3p high
11 S XVI 2p 24
12 Si XIV 5p high
13 S XV 2p (w) 14
14 S XV 2p (z) 14
15 Si XIV 3p 16
16 Si XIII 5p high
17 Si XIII 4p 11
18 Si XIII 3p 10
19 Si XII 3p sat. high

---
DEM distributions
B5.6
C5.8
X1.0

---
SphinX efficiency
0.5 – 15 keV

---
SphinX spectra – 25 January 2003
B5.6

---
SphinX spectra – 25 January 2003
B5.6

---
SphinX spectra – 22 February 2003
C5.8

---
SphinX spectra – 22 February 2003
C5.8

---
SphinX spectra – 3 August 2002
X1.0

---
SphinX spectra – 3 August 2002
X1.0

---
SphinX spectra – all flares
 3 Aug 2002 X1.0
22 Feb 2003 C5.8
25 Jan 2003 B5.6

---
SphinX spectra – all flares
 3 Aug 2002
22 Feb 2003
25 Jan 2003

---
What was dane?
We selected
10 spectral bands
for DEM calaculations

---
Spectral bands for DEM
Photons/cm2/s/keV

---
Spectral bands for DEM
1: 0.5 keV – 1.25 keV 9.9 Å - 24.8 Å
Elements:
        Fe
        Ne
        Cr
        Ni
        Co
        Na
        Mn
        Ca
       O
       Ar
       N
       Si
       S

---
Spectral bands for DEM
2: 1.25 keV – 1.67 keV 7.4 Å - 9.9 Å
Elements:
        Mg
        Fe
        Al
        Cr
        Ni
        Na

---
Spectral bands for DEM
3: 1.67 keV – 2.15 keV 5.77 Å - 7.42 Å
Elements:
       Si
        Al
        Mg
        Ni
        P

---
Spectral bands for DEM
4: 2.3 keV – 2.7 keV 4.59 Å - 5.39 Å
Elements:
        S
        Si
        P

---
Spectral bands for DEM
5: 2.95 keV – 3.3 keV 3.76 Å - 4.20 Å
Elements:
        Ar
        S
        Cl

---
Spectral bands for DEM
6: 3.6 keV – 4.1 keV 3.02 Å - 3.44 Å
Elements:
        Ca
        Ar
        K

---
Spectral bands for DEM
7: 6.2 keV – 7.0 keV 1.77 Å - 1.99 Å
Elements:
        Fe

---
Spectral bands for DEM
8: 7.5 keV – 8.0 keV 1.55 Å - 1.65 Å
Elements:
        Fe
        Ni

---
Spectral bands for DEM
9: 8.0 keV – 8.5 keV 1.46 Å - 1.55 Å
Elements:
        Fe
        Ni

---
Spectral bands for DEM
10: 10.0 keV – 10.01 keV 1.22 Å - 1.24 Å
Elements:
        Ni

---
Emission functions

---
 DEMs
SphinX
RESIK

---
The end